## Slide 1: Module 1
software requirements and
examples of digital twins

## Slide 2: Software requirements
Simulation Software Siemens NX MCD
Simulation Tool PLC SIM Adv.
PLC Programming Software Siemens TIA-Portal
Creating a Soft-PLC as a
connector between
MCD and TIA Portal

## Slide 3: Examples of digital twins

## Slide 4: Examples of digital twins
conveyor belt
with light beams
workpiece handling
physical bodies
lift handling
Material sorting (metal and non metal)
CP lab transfer track

## Slide 5: Physical bodies
The digital models can be given physical properties (e.g. density, friction, ...). Thus, the model behavior corresponds to the real behavior. The bodies roll down the ramp at different speeds. Also bodies can leave the ramp.

## Slide 6: Conveyor belt with light beams
Different bodies can be transported on the belt. Modelled light barriers give signals (e.g. to a controller) that can be further processed.

## Slide 7: Workpiece handling
Digital pneumatic cylinders extend and transmit a force to the workpieces so that they reach the next conveyor belt. The cylinders can be integrated into PLC programming and controlled.

## Slide 8: Lift handling
Similarly, a vertical production line can also be simulated using the physical properties. In this example, one cylinder is used as a lifting cylinder and the other as an extension cylinder. Both are controlled by a PLC.

## Slide 9: Sorting station
In the material sorting system, a distinction is made between metallic and non-metallic workpieces. The material properties are given to the workpieces as part of the creation of a digital twin. The system can sort out metallic or non-metallic workpieces on the basis of PLC programming.

## Slide 10: CP Lab transfer track
Here you can see the digital twin of the transfer track of a production plant. A workpiece (red) is transported through the production line on the belt with the help of a workpiece carrier. The transfer belt is controlled by a PLC. It has several sensors at the respective ends and in the middle. There is also a stopper in the middle. This allows the movements that are crucial for production to be realized.

## Slide 11: CP Lab transfer with turning application
Here you can see the digital twin of the transfer track with the turning application on top.
This is the master piece of our digital twin. With this simulation tool a hole class can create plc programs in the same time and test their solutions directly.