## Slide 1: Digital twin
Funded by the European Union. Views and opinions expressed are however those of the author(s) only and do not necessarily reflect those of the European Union or the European Education and Culture Executive Agency (EACEA). Neither the European Union nor EACEA can be held responsible for them.

## Slide 2
Ruben Rolighed

## Slide 3: Introduction
The Digital Twin consist of a simple 3D model that has been equipped with advanced physical properties.
The Digital twin also has an interface of mutual communication with the physical Machine.
In this course we are going to focus on building the 3D model in Inventor.
When the 3D model is finished, it will be exported to Siemens NX, where the physical properties will be added to the twin.

## Slide 4: Content
Drawing basics
  Introduction to inventor
  Create simple box (Machine base)
  Sketch and Extrude
Assemblies
  Create an assembly file
  Add parts to an assembly
  Create and modify parts inside an open assembly
Subassemblies and relationships
  Creating a Pusher subassembly
  Connecting parts with relationships
  Placing the subassembly in the main assembly
Modelling the conveyor
  Sketch - Arc
  Mate relationship with offset
Import CAD from vendor
Export to STEP

## Slide 5: Drawing basics Video 1
Introduction to Inventor – Project folder, file type, Units and drawing standard
Create a simple 3D box, the machine base plate
Sketch and Extrude

## Slide 6: Welcome screen
Project folders
    Create new project
    File location
Application settings
  Units
  ISO standard
Create file
  Part
  Assembly
  Drawing
  Presentation

## Slide 7: Welcome screen
An Inventor project will typically consist of severel folders and files of different types. To avoid making a huge pool of files belonging to all different projects, it is recommended to create a project folder for each project.
Click the project folder menu (3 dots) and open the settings
Project folders
    Create new project
    File location
Application settings
  Units
  ISO standard
Create file
  Part
  Assembly
  Drawing
  Presentation

## Slide 8: Welcome screen
An Inventor project will typically consist of severel folders and files of different types. To avoid making a huge pool of files belonging to all different projects, it is recommended to create a project folder for each project.
In the top window, the existing project folder and their locations are shown
Click ”New” to create a new project folder
Project folders
    Create new project
    File location
Application settings
  Units
  ISO standard
Create file
  Part
  Assembly
  Drawing
  Presentation

## Slide 9: Welcome screen
An Inventor project will typically consist of severel folders and files of different types. To avoid making a huge pool of files belonging to all different projects, it is recommended to create a project folder for each project.
In the top window, the existing project folder and their locations are shown
Click ”New” to create a new project folder
Vault folder is a cloud project for collaboration between multiple user. Single user is, like the name elaborates very well, for a single user to work on.
Project folders
    Create new project
    File location
Application settings
  Units
  ISO standard
Create file
  Part
  Assembly
  Drawing
  Presentation

## Slide 10: Welcome screen
Every time we create a file, it is created with some default settings. In this project, we want the documents created in ISO standards and with metric measuring units.
These settings are chosen as default in the following way:
Project folders
    Create new project
    File location
Application settings
  Units
  ISO standard
Create file
  Part
  Assembly
  Drawing
  Presentation
In the top left corner of the welcome screen, press ”Application Options”

## Slide 11: Welcome screen
Project folders
    Create new project
    File location
Application settings
  Units
  ISO standard
Create file
  Part
  Assembly
  Drawing
  Presentation
In the ”File” tab, press ”Configure Default Template”
I popup ruden kan man vælge måleenhed og default tegningsstandard. Afslut med ”OK”

## Slide 12: Welcome screen
Project folders
    Create new project
    File location
Application settings
  Units
  ISO standard
Create file
  Part
  Assembly
  Drawing
  Presentation
To create a new Part file from the welcome screen, can be done in two ways. If we open the drop-down menu, we can choose between the four file types. Press ”Part” and a standard Part file will be created.

## Slide 13: Welcome screen
Project folders
    Create new project
    File location
Application settings
  Units
  ISO standard
Create file
  Part
  Assembly
  Drawing
  Presentation
If we press ”New”, a window will open with additional options like for example ”Sheet metal”. In this project we will only create Standard parts.

## Slide 14: Welcome screen
Project folders
    Create new project
    File location
Application settings
  Units
  ISO standard
Create file
  Part
  Assembly
  Drawing
  Presentation
If we press ”New”, a window will open with additional options like for example ”Sheet metal”. In this project we will only create Standard parts.
When a file is created, it will be opened in the Inventor Workspace.

## Slide 15: Inventor Workspace
Menu - Ribbon
    File
    Assemble
    3D Model
    Sketch
    Tools for modelling
  Project tree
    Folder structure of the open document
  Graphics window
    Navigation
    Visualization
  File Tabs
    Open documents

## Slide 16: Creating the first Part ”Machine base”
2D sketch
  Create sketch
  Place in Plane
  Draw a sketch
When drawing a CAD model(Part) in inventor, the workflow is usually:
Create a Part(.ipt)
Chose or create a Plane
Place and draw a sketch in the plane
Create a 3D model from the sketch
Modify body
When multiple Parts exist, we can assemble them in an assembly(.iam)
If the CAD model needs to be produced in real life, we can create Drawings for production purposes(.DWG files).
If the model is to be introduced to customers or co-workers, it can be presented in a Presentation file(.ipn).
Other workflows exist, but this one is the most common one.
3D model
  Create body(solid) from sketch
  Modify/adjust body

## Slide 17: Creating the first Part ”Machine base”
2D sketch
  Create sketch
  Place in Plane
  Draw a sketch
To create a sketch, press the button “Start 2D sketch”. Now the Origin planes will get visible and we have to chose one of them for the sketch.
3D model
  Create body(solid) from sketch
  Modify/adjust body
Hover the mouse over the planes.
When the desired plane is green, left-click with the mouse

## Slide 18: Creating the first Part ”Machine base”
2D sketch
  Create sketch
  Place in Plane
  Draw a sketch
Now the sketch is connected to a plane and ready for drawing. Draw the desired shape on the sketch and add dimensions to the sides.
3D model
  Create body(solid) from sketch
  Modify/adjust body
Here the two-point rectangle is chosen and placed at the center of the sketch.
Write the length of the first side. Press “Tab” to jump to the other side.
Finish the rectangle with “Enter”
When sketch is ready, press “Finish”
TAB

## Slide 19: Creating the first Part ”Machine base”
2D sketch
  Create sketch
  Place in Plane
  Draw a sketch
Now it is time to add the 3rd dimension. In 3D Model ribbon, there is a group of tools named“Create” which are all for creating solids.
3D model
  Create body(solid) from sketch
  Modify/adjust body
For this part, we just need a simple box or “plate”. It can be created with “Extrude”.
Press Extrude and click the rectangular profile on the sketch.
An extrusion window will open. Here we can choose the direction, the distance and a name for the solid.
Finish with “OK”

## Slide 20: Assemblies Video 2
Create an assembly file
Add parts to an assembly
Create and modify parts inside an open assembly

## Slide 21: Assemblies
Assemblies can be created from the Welcome screen or from the workspace.
Create Assembly file
  Name the assebly
To create an Assembly file, open the drop-down menu in the welcome screen and choose Assembly(.iam)
Place part in assembly
Create new parts in an open assembly
  Create a workpiece on the machine base
  Navigating between parts in assembly

## Slide 22: Assemblies
Assemblies can be created from the Welcome screen or from the workspace.
Create Assembly file
  Name the assebly
To rename the new assembly, double click the assembly root in the project tree.
Place part in assembly
Create new parts in an open assembly
  Create a workpiece on the machine base
  Navigating between parts in assembly

## Slide 23: Assemblies
When an assembly is open, it is possible to place existing parts in the assembly. It is also possible to create and modify parts inside the open assembly.
To place an existing part in the assembly, click “Place”
Create Assembly file
  Name the assebly
Place part in assembly
Create new parts in an open assembly
  Create a workpiece on the machine base
  Navigating between parts in assembly

## Slide 24: Assemblies
When an assembly is open, it is possible to place existing parts in the assembly. It is also possible to create and modify parts inside the open assembly.
Choose the desired part to add it to the assembly
Create Assembly file
  Name the assebly
Place part in assembly
Create new parts in an open assembly
  Create a workpiece on the machine base
  Navigating between parts in assembly

## Slide 25: Assemblies
When an assembly is open, it is possible to place existing parts in the assembly. It is also possible to create and modify parts inside the open assembly.
After choosing a part, the part must be placed in the assembly by left-clicking the mouse in the graphics area
Create Assembly file
  Name the assebly
Place part in assembly
Create new parts in an open assembly
  Create a workpiece on the machine base
  Navigating between parts in assembly

## Slide 26: Assemblies
When an assembly is open, it is possible to place existing parts in the assembly. It is also possible to create and modify parts inside the open assembly.
To create a new part inside the open assembly, click “Create” in the Components group in the Assembly Ribbon.
Create Assembly file
  Name the assembly
Place part in assembly
Create new parts in an open assembly
  Create a workpiece on the machine base
  Navigating between parts in assembly
Name the new part in the popup window

## Slide 27: Assemblies
When an assembly is open, it is possible to place existing parts in the assembly. It is also possible to create and modify parts inside the open assembly.
Now the mouse is holding the new part.
Create Assembly file
  Name the assembly
Place part in assembly
Create new parts in an open assembly
  Create a workpiece on the machine base
  Navigating between parts in assembly
If the mouse is hovered over an existing part, a face will be highlighted in green. If you place the part on the highlighted face, the origin of the new part will be constrained to the face.

## Slide 28: Assemblies
Create Assembly file
  Name the assembly
Place part in assembly
Create new parts in an open assembly
  Create a workpiece on the machine base
  Navigating between parts in assembly
Now the new part is created inside the assembly.
Notice the new branch on the project tree.
And notice that the new background of the new part is white, while the rest of the project tree is grayed out. This means that the new part “Workpiece” is open and the rest of the assembly is deactivated.

## Slide 29: Assemblies
Create Assembly file
  Name the assembly
Place part in assembly
Create new parts in an open assembly
  Create a workpiece on the machine base
  Navigating between parts in assembly
Now the new part is created inside the assembly.
To close the new part and reactivate the entire assembly, press “Return”
Now you can start designing the part, by placing a 2D sketch on a plane or on a surface

## Slide 30: Subassemblies & Relationships Video 3
Creating a Pusher subassembly
Connecting parts with relationships
Placing the subassembly in the main assembly

## Slide 31: Subassemblies & relationships
Create a subassembly
  Assembly inside assembly
Relationships
  Joints
  Constrains
A sub assembly is just a normal assembly who lives inside a parent assembly. Subassemblies can also live inside subassemblies.
Assembly
SubAssembly
SubAssembly
Part
Part
Part
Project Geometry

## Slide 32: Subassemblies & relationships
Create a subassembly
  Assembly inside assembly
Relationships
  Joints
  Constrains
To create a structure of Assembly/Subassemblies, simply create an Assembly file and Place it inside another Assembly.
1
3
2
Project Geometry

## Slide 33: Subassemblies & relationships
Create a subassembly
  Assembly inside assembly
Relationships
  Constrains
  Joints
Relationships are used to connect parts and assemblies to each other with a defined set of rules.
Both groups are used in video 3 as an example.
Project Geometry
Constrains
Constrains are very specific limitations made for a geometry in a sketch or a component. Examples could be:
Line1=12mm.
Angle between Line1. and Line2 = 60°.
Face1 and face2 = Tangent.
Face1 and face2 = Mated.
Joint
Joint relationships are preconfigured tools consisting of several Constrains:
Rigid is a relationship without movement allowed.
Rotational has a defined rotatin allowed
Slider allows linear movement
Planar allows 2D movement in a specified plane

## Slide 34: Subassemblies & relationships
Create a subassembly
  Assembly inside assembly
Relationships
  Constrains
  Joints
Project is a handy tool that “copies” a geometry to a sketch, so you do not need to draw the geometry again.
Project Geometry

## Slide 35: Modelling the conveyor Video 4
Sketch - Arc
Mate relationship with offset

## Slide 36: Modelling the conveyor
Sketch Arcs
  Tangent arc
Relationship
  MATE with offset
The conveyor is very simple. It consist of a Sketch with a box. On each end of the box, half a circle is connected. 3rd dimension is a simple Extrusion of the box and arcs.

## Slide 37: Modelling the conveyor
Sketch Arcs
  Tangent arc
Relationship
  MATE with offset
Arcs can be crated in three different methos: Three Point, Center and Tangent
Three Point Arc is drawing an arc from point 1, through point 2, to point 3
Tangent Arc must be connected with two points to existing geometry and will size the arc to be tangent with the two geometrys, like in video 4.
Center Point Arc is created by placing an Arc center and the two end points.

## Slide 38: Modelling the conveyor
Sketch Arcs
  Tangent arc
Relationship
  MATE with offset
Arcs can be crated in three different methods: Three Point, Center and Tangent
Three Point Arc is drawing an arc from point 1, through point 2, to point 3
Tangent Arc must be connected with two points to existing geometry and will size the arc to be tangent with the two geometrys, like in video 4.
Center Point Arc is created by placing an Arc center and the two end points.

## Slide 39: Import CAD from vendor Pusher 2 Video 5
Import STEP file from Festo

## Slide 40: Import model from Vendor
Find CAD from Festo
  STEP
  File to Inventor project folder
  Import to project
Inventor can import various CAD file types. The most commonly used file type across different CAD-software is STEP.
Relationship
  MATE with offset
  Adjust position on the base plate

## Slide 41: Import model from Vendor
Find CAD from Festo
  STEP
  File to Inventor project folder
  Import to project
It is good practice to always keep all implemented files inside the Inventor project folder.
Therefor we will move the downloaded file from Download folder to project folder before implementing it in the the assembly.
Downloads
Festo STEP
Project folder
Relationship
  MATE with offset
  Adjust position on the base plate

## Slide 42: Import model from Vendor
Find CAD from Festo
  STEP
  File to Inventor project folder
  Import to project
In the “Assemble” tab, make sure to have the Main Assembly active and presse the “Place Imported CAD Files” button. Find the file in the browser to add it.
Relationship
  MATE with offset
  Adjust position on the base plate

## Slide 43: Import model from Vendor
Find CAD from Festo
  STEP
  File to Inventor project folder
  Import to project
Choose the desired import settings and press OK.
In this example, the default settings has been used for the import.
Relationship
  MATE with offset
  Adjust position on the base plate

## Slide 44: Import model from Vendor
Find CAD from Festo
  STEP
  File to Inventor project folder
  Import to project
Place the imported component in some random place in the graphics window.
Use a Relationship tools to fixate the component in the assembly with relevant rules and position.
Relationship
  MATE with offset
  Adjust position on the base plate

## Slide 45: Import model from Vendor
Find CAD from Festo
  STEP
  File to Inventor project folder
  Import to project
Press the “Constrain” button
Choose the MATE-option in the Constrain window.
Choose the first face with a left-click.
Relationship
  MATE with offset
  Adjust position on the base plate

## Slide 46: Import model from Vendor
Find CAD from Festo
  STEP
  File to Inventor project folder
  Import to project
Then click the face that the cylinder must MATE with
Relationship
  MATE with offset
  Adjust position on the base plate

## Slide 47: Import model from Vendor
Find CAD from Festo
  STEP
  File to Inventor project folder
  Import to project
Relationship
  MATE with offset
  Adjust position on the base plate
Now offset the MATE by dragging the arrow between the two faces or write the desired offset into the Constrain window.
Finish with “OK”

## Slide 48: Import model from Vendor
Find CAD from Festo
  STEP
  File to Inventor project folder
  Import to project
Relationship
  MATE with offset
  Adjust position on the base plate
Lastly, drag the Festo cylinder to the optimal position with the mouse.
The component still have two dimensions of freedom to do this.

## Slide 49: Export project to STEP Video 6
Export the entire CAD drawing to STEP file

## Slide 50: Export to STEP
Activate Main assembly
Export the project
  Export to STEP
In the FILE tab, choose Export / CAD Format

## Slide 51: Export to STEP
Name the Export file
Choose the location for the file
Choose the file type and press save
Activate Main assembly
Export the project
  Export to STEP

## Slide 52: Thank you
Want to learn more?
Inventor tutorials in the Welcome Screen
Youtube